## Slide 1: Local Road Safety Plan Draft Findings
September 28, 2020

## Slide 2: Presentation Overview
What is the Collier County Local Road Safety Plan (LRSP)
Data Analysis and Findings
Recommendations
Next Steps

## Slide 3: LRSP Overview
Process recommended by FHWA as “Proven Safety Countermeasure”
Data Driven
Multi-Disciplinary

## Slide 4: Countywide Crash Data Analysis
VMT Distribution of Collier County and Florida by Functional Class
  Collier County relies more on signalized arterial and major collector roadways than the state as a whole.
  Generally these roadways have worse safety outcomes than limited access highways and lower speed minor collector and local streets.
Roadway Functional Classification | Florida |  | Collier |  | Crash Characteristics
Interstate, Turnpike & Freeways | 26% |  | 21% |  | Limited Access, Low Crashes/VMT
Other Principle Arterials | 25% | 50% | 16% | 59% | Higher Speed, More Conflict Points
Minor Arterials | 15% |  | 29% |  | 
Major Collectors | 11% |  | 14% |  | 
Minor Collectors | 2% | 23% | 2% | 20% | Lower Speed, Less Severe Crashes
Locals | 21% |  | 18% |  | 

## Slide 5: Data Analysis
 | Florida | Collier County | Collier County vs. Florida
Crashes/100k Pop. | 1,904 | 1,413 | 74%
Fatalities/100k Pop. | 15 | 11 | 73%
Injuries/100k Pop. | 1,204 | 806 | 67%
Overall, Collier County performs better than the State of Florida

## Slide 6: Data Analysis: Major Roadway Focus
Excluding I-75, arterial and collector roads account for:
  74% of severe crashes
  77% of all reported public roadway crashes
Chart: 
| Interstate | Arterials and Collectors | All Other Public Roads
 | 0.090628 | 0.73944 | 0.16993
 | 0.049287 | 0.76618 | 0.18453
All Crashes
Severe Crashes

## Slide 7: Data Analysis: Maintenance Authority
Crash Distribution by Major Roadway Maintenance Authority:
  County-maintained roads account for 62% of severe crashes and 72% of all crashes.
  Crash distribution is roughly proportional to vehicle miles traveled for each maintenance authority.
Chart: 
| State | County | City
Percent VMT | 0.30203 | 0.66908 | 0.028894
Percent Severe Crashes | 0.33844 | 0.61978 | 0.041783
Percent All Crashes | 0.25009 | 0.71858 | 0.031332
All Crashes
Severe Crashes
Vehicle Miles Travelled

## Slide 8: Data Analysis: Crash Types
Crash Type Distribution:
Rear end crashes are the most common overall crash type.
Several crash types have out-sized severity ratios compared with overall frequency.
Chart: 
| Category | Pedestrian | Run Off Road | U-Turn | Single Vehicle | Hit Non-Fixed Object | Head On | Bike | Right Turn | Left Turn | Unknown | Hit Fixed Object | Angle | Sideswipe | Rear End
Severe Crashes | 0 | 0.091658 | 0.026777 | 0.012358 | 0.043254 | 0.0051493 | 0.027806 | 0.086509 | 0.014418 | 0.12358 | 0.058702 | 0.15242 | 0.16066 | 0.027806 | 0.1689
All Crashes | 0 | 0.0082587 | 0.0094626 | 0.010426 | 0.010859 | 0.010931 | 0.012183 | 0.012713 | 0.023933 | 0.055716 | 0.0594 | 0.079625 | 0.11013 | 0.12386 | 0.4725
47.3%

## Slide 9: Data Analysis
 | High Severity Ratio | Low Severity Ratio
High Severity Frequency (> 5% of All Severe Crashes) | Bike Pedestrian Left-Turn Angle Hit Fixed Object | Rear-End Unknown/Other
Low Severity Frequency (<5% of All Severe Crashes) | Head-On Single Vehicle U-Turn Run Off Road | Sideswipe Right-Turn Hit Non-Fixed Object

## Slide 10: Data Analysis: Age
At Fault Driver Age:
Younger and middle-aged adults are over-represented in reported crashes.
Older drivers may have less exposure (fewer miles travelled).
Chart: 
| 85+ | 80-84 | 75-79 | 70-74 | 65-69 | 60-64 | 55-59 | 50-54 | 45-49 | 40-44 | 35-39 | 30-34 | 25-29 | 20-24 | 15-19 | 14 and Under
Percent of Crashes | 0.025427 | 0.026133 | 0.036481 | 0.042753 | 0.049548 | 0.053207 | 0.06575 | 0.071918 | 0.07129 | 0.067318 | 0.075681 | 0.087022 | 0.10411 | 0.12727 | 0.095124 | 0.00096692
Percent of Population | 0.048266 | 0.046305 | 0.069904 | 0.077733 | 0.08135 | 0.070766 | 0.063711 | 0.059112 | 0.054747 | 0.047888 | 0.04844 | 0.047909 | 0.046641 | 0.04448 | 0.052963 | 0.13979

## Slide 11: Data Analysis: Age
70%
30%

## Slide 12: Data Analysis: Annual Trends
Chart: 
| 2014 | 2015 | 2016 | 2017 | 2018
 | 7633 | 8406 | 8926 | 8123 | 8444
Annual Trend:
Crashes trending upward year-over-year, but trend is unstable.
Trend

## Slide 13: Data Analysis: Seasonal Distribution
Average Crashes per Month:
Average of 702 reported crashes per month.
Monthly trends generally follow overall seasonal patterns.
Chart: 
| Jul | Aug | Sep | Oct | Nov | Dec | Jan | Feb | Mar | Apr | May | Jun
 | 570 | 627 | 614 | 790 | 708 | 737 | 818 | 725 | 852 | 737 | 678 | 571
Average

## Slide 14: Data Analysis: Citations
Most Common Moving Violations:
  Exceeding posted speed most common citation
  Disregard traffic control or traffic signal are second most common
Chart: 
Chart: 
| Exceeding Posted Speed | Disregard Traffic Control Device | Disregard Traffic Signal | Driving with Revoked or Suspsended License (without knowledge) | Failure to Yield ROW | All Other (< 5%)
 | 12427.6 | 2182 | 1480.4 | 1154.4 | 1053.2 | 3849.6667
 | 0.56113 | 0.098522 | 0.066843 | 0.052124 | 0.047554 | 0.17382

## Slide 15: Data Analysis: Citations
Traffic Citation Data:
  Collier County issues fewer citations than the state average per capita and per vehicle miles travelled.
  FHP and Collier Sheriff issue the bulk of traffic citations.
Chart: 
| Florida Highway Patrol | City Police Department | Sheriff's Office | Other
 | 0.3897 | 0.15488 | 0.44663 | 0.0087921
State and County | Violations (2014-18) | Total VMT (2014-18) | Citations per 100K VMT | Population | Citations per 100K Pop.
Florida | 1,978,741 | 582,491,060 | 340 | 20,159,183 | 9,816
Collier | 22,136 | 9,939,709 | 223 | 351,121 | 6,304
Brevard | 29,592 | 17,784,554 | 166 | 568,367 | 5,206
Escambia | 24,176 | 9,657,445 | 250 | 310,556 | 7,785
Lee | 83,614 | 20,667,894 | 405 | 682,448 | 12,252
Manatee | 23,208 | 10,038,803 | 231 | 358,616 | 6,472
Sarasota | 33,880 | 12,052,890 | 281 | 400,694 | 8,455

## Slide 16: Data Analysis: Survey
Over 1,000 responses

## Slide 17: Data Analysis: Survey
Chart: 
| Daily | More than 4 times a week | 2-4 times a week | Once a week | Less than once a month
 | 0.7546 | 0.14062 | 0.087316 | 0.015625 | 0.0018382
Frequency of Motor Vehicle Use

## Slide 18: Data Analysis Survey
Chart: 
| Roadway design | People driving under the influence of alcohol, drugs, medications or other substances | Pedestrians and bicyclists sharing the roadway | People not wearing seatbelts | Aging drivers | Motorcyclists | Commercial vehicles operating on local roads | Speeding and aggressive driving | Teen drivers | People using cell phones or doing other activities while driving | Inadequate roadway lighting or traffic signals | Construction or utility work zones | People who do not know the “rules of the road”
 | 0.17615 | 0.23028 | 0.27248 | 0.011009 | 0.43028 | 0.045872 | 0.14128 | 0.59266 | 0.048624 | 0.64037 | 0.14587 | 0.066055 | 0.40917
Driver Behavior Concerns:

## Slide 19: Data Analysis: Survey
Chart: 
| Strongly agree | Somewhat agree | Somewhat disagree | Strongly disagree | No opinion
 | 0.039595 | 0.16575 | 0.1814 | 0.33517 | 0.27808
Chart: 
| Strongly agree | Somewhat agree | Somewhat disagree | Strongly disagree | No opinion
 | 0.14299 | 0.39022 | 0.17712 | 0.1393 | 0.15037
Biking Walking
I feel safe and comfortable while biking/walking in Collier County…

## Slide 20: Data Analysis: Findings
Collier County has better safety performance than the State.
Most crashes occur along major roadways.
About 2/3 of these occur along County-maintained roads
Older road users do not disproportionately contribute to crashes in Collier County, likely due to reduced exposure
Fewer traffic citations per capita and per vehicle mile of travel are issued in Collier County than average
Non-motorized road user, angle, left-turn, and lane departure crashes account for 30% of all crashes but result in 72% of severe injuries and 89% of fatalities.
Rear-end and sideswipe crashes result in a significant number of incapacitating injuries due to their frequency.

## Slide 21: Data Analysis: Emphasis Areas
 | All Crashes | Non-Motorized | Intersection | Lane Departure | Same Direction
Total Crashes | 38,887 | 862 | 6,819 | 3,829 | 23,419
Injury Crashes | 3,469 | 448 | 1,030 | 567 | 1,111
Total Injuries | 4,719 | 470 | 1,621 | 747 | 1,492
Total Serious Injuries | 928 | 136 | 326 | 201 | 187
Fatal Crashes | 148 | 38 | 39 | 53 | 10
Total Fatalities | 160 | 38 | 40 | 64 | 10
Severity Ratio | 2.4% | 15.8% | 4.8% | 5.2% | 0.8%
Percent of All Crashes | NA | 2% | 18% | 10% | 60%
Percent of Severe Injuries | NA | 15% | 35% | 22% | 20%
Percent of Fatalities | NA | 24% | 25% | 40% | 6%

## Slide 22: Infrastructure Strategies
Infrastructure Strategies | Non-Motorized | Intersection | Lane Departure | Same Direction
Speed Management |  |  |  | 
Alternative Intersections (ICE Process) |  |  |  | 
Intersection Design Best Practices for Pedestrians |  |  |  | 
Median Restrictions/Access Management |  |  |  | 
Right Turn Lanes | ? |  |  | 
Signal Coordination | ? |  |  | 
Rural Road Strategies including: |  |  |  | 
Paved shoulder |  |  |  | 
Safety edge |  |  |  | 
Curve geometry, delineation, and warning |  |  |  | 
Bridge/culvert widening/attenuation |  |  |  | 
Guardrail/ditch regrading/tree clearing |  |  |  | 
Isolated intersection conspicuity/geometry |  |  |  | 
Shared Use Pathways, Sidewalk Improvements |  |  |  | 
Mid-Block Crossings & Median Refuge |  |  |  | 
Intersection Lighting Enhancements |  |  |  | 
Autonomous Vehicles (Longer-Term) | TBD |  |  | 
? = Possible Contra-indications |  |  |  | 

## Slide 23: Infrastructure: Speed Management
Adopt/Adapt FDOT’s Context Classification System to the County’s major roadways.
Using the classification system, establish target speeds
Prioritize engineering studies to identify design interventions to achieve targets
Consider signal operations (density, progression, & cycle length) as speed management strategies

## Slide 24: Infrastructure: Alternative Intersections
Adopt/Adapt FDOT’s Intersection Control Evaluation (ICE) process
Identify candidate intersections
Conduct “Stage 1” analysis to screen and prioritize candidates

## Slide 25: Infrastructure: Pedestrian Design Best Practices
Design/retrofit major intersections with pedestrian design best practices in mind.
Identify candidate intersections and prioritize retrofit projects

## Slide 26: Infrastructure: Pedestrian Mid-Block Crossing
Provide raised medians or refuge islands along roadways with painted medians to help calm traffic and make it safer to cross the street.
Consider providing mid-block crossings with appropriate supplemental devices where needed.

## Slide 27: Infrastructure: Low-Stress Bike Facilities
Provide separated bike facilities along higher speed (40+ mph) major roadways
Consider the Level of Traffic Stress criteria as a performance measure for bicycle facilities (in lieu of FDOT BLOS)

## Slide 28: Infrastructure: Low-Stress Bike Facilities
Apply systemic improvements to rural highways including
  Pavement edge treatments
  Curve warning, delineation
  Isolated intersection warning
  Clear zone management

## Slide 29: Infrastructure: Other
Continue access management approaches in suburban areas but consider new signals in urban areas.
Maintain safety focus on right turn lanes and be cautious of using right turn lanes in urban areas primarily to add capacity
Apply signalization strategies that consolidate traffic platoons and help to manage speeds
Adopt/Adapt FDOT’s intersection lighting standard to Collier County major roadways.

## Slide 30: Non-Infrastructure Strategies
Non-Infrastructure Strategies | Intersection | Lane Departure | Non-Motorized | Rear End/ Sideswipe
Traffic Enforcement |  |  |  | 
Targeted Speed Enforcement |  |  |  | 
Red Light Running Enforcement |  |  |  | 
Automated Enforcement |  |  |  | ?
Pedestrian Safety Enforcement |  |  |  | 
Bike Light and Retroreflective Material Give-Away |  |  |  | 
Young Driver Education |  |  |  | 
WalkWise/BikeSmart or Similar Campaign |  |  |  | 
Continuing Education |  |  |  | 
Safety Issue Reporting |  |  |  | 
Vision Zero Policy |  |  |  | 
? = Possible Contraindication |  |  |  | 

## Slide 31: Non-Infrastructure: Law Enforcement
Align law enforcement with emphasis areas focusing on speed management and intersection crashes.
Consider applying for FDOT High Visibility Enforcement Grants as a way to educate pedestrians and cyclists and check driver yielding behavior.
Consider revisiting automated enforcement as a way to free-up human enforcement resources.

## Slide 32: Non-Infrastructure: Give-Aways
Provide retroreflective materials and bike light kits

## Slide 33: Non-Infrastructure: Teen Safe Driving
Engage with Florida Teen Safe Driving Coalition to identify and intitiate programs to reduce young driver crashes in Collier County.

## Slide 34: Non-Infrastructure: Adult Education
Consider implementing an adult education seminar program similar to the “WalkWise” program in the Tampa Bay area.

## Slide 35: Non-Infrastructure: Safety Concern Database
Consider implementing an online system to allow safety partners (or the general public) to post non-emergency safety concerns.

## Slide 36: Non-Infrastructure: Vision Zero
Begin identifying local champions to implement a Vision Zero policy

## Slide 37: Next Steps
Incorporate Committee Feedback
Finalize Report and Implementation Plan
Present to the MPO Board

## Slide 38: Contact:
Demian Miller, AICP Anne McLaughlin
Principal Executive Director
Tindale Oliver Collier MPO
813-224-8862 239-252-5884
dmiller@tindaleoliver.com anne.mclaughlin@colliercountyfl.gov

## Slide 39: Other Crash Data Stats

## Slide 40: Countywide Crash Data Analysis
Crash Distribution by Major Roadway Number of Lanes:
  2-lane major roadways have proportionately more severe crashes per vehicle mile travelled than multi-lane roads.
  This could indicate rural highway safety issues
Chart: 
| 6 or More | 4 Lanes | 2 Lanes
Percent Daily VMT | 0.5041 | 0.18326 | 0.31264
Percent Severe Crashes | 0.37931 | 0.21552 | 0.40517
Percent All Crashes | 0.51661 | 0.21262 | 0.27076
All Crashes
Severe Crashes
Vehicle Miles Travelled

## Slide 41: Countywide Crash Data Analysis
Chart: 
| East of CR 951 | CR 951 and to the West
 | 0.40139 | 0.59861
 | 0.42735 | 0.57265
 | 0.28027 | 0.71973
Major Roadway Crashes* by Sub-Area:
  The Western (urban) part of the county accounts for 72% of all crashes and 57% of severe crashes—roughly proportional to vehicle miles of travel.
  The eastern (rural ) part of the county has fewer crashes overall, but a greater proportion of severe crashes.
All Crashes
Severe Crashes
Vehicle Miles Travelled

## Slide 42: Countywide Crash Data Analysis
Chart: 
| Daylight | Dark-Lighted | Dark-Not Lighted | Dusk | Dawn
 | 0.58041 | 0.20103 | 0.15155 | 0.049485 | 0.017526
 | 0.77856 | 0.127 | 0.054187 | 0.023417 | 0.016837
Lighting Condition
  78% of all crashes occur during daylight hours.
  Only 58% of severe crashes occur during daylight.
All Crashes
Severe Crashes

## Slide 43: Countywide Crash Data Analysis
Chart: 
| Daylight | Dark-Lighted | Dark-Not Lighted | Dusk | Dawn
 | 0.77856 | 0.127 | 0.054187 | 0.023417 | 0.016837
 | 0.70453 | 0.14818 | 0.096717 | 0.027507 | 0.02307
 | 0.51795 | 0.21538 | 0.18462 | 0.05641 | 0.025641
Non-Motorized Crashes by Lighting Condition:
  Non-motorized crashes are more likely to occur outside of daylight hours.
  This is especially true of severe non-motorized crashes.
Severe
Non-Motorized
All
Non-Motorized
All Crashes

## Slide 44: PUBLIC SURVEY RESULTS

## Slide 45: Live/Work & Age
Chart: 
| I live in Collier County year-round | I live in Collier County for part of the year | I work in Collier County | I live in the region and visit Collier County for shopping and recreation | I own a business in Collier County | I am a visitor to Collier County
 | 0.88306 | 0.072744 | 0.43002 | 0.075506 | 0.10221 | 0.01105
Chart: 
| 18-24 | 25-34 | 35-44 | 45-54 | 55-64 | 65+
 | 0.032288 | 0.13469 | 0.23708 | 0.20387 | 0.20941 | 0.18266
Please describe yourself by checking all that apply
What is your age?

## Slide 46
Chart: 
| Daily | More than 4 times a week | 2-4 times a week | Once a week | Less than once a month
 | 0.7546 | 0.14062 | 0.087316 | 0.015625 | 0.0018382
Chart: 
| 0-10 minutes | 10-20 minutes | 20-30 minutes | 30 minutes or more
 | 0.047794 | 0.16544 | 0.22151 | 0.56526
How often do you drive a motor vehicle (Choose one)?
How much time do you typically spend traveling each day (Choose one)?

## Slide 47
Chart: 
| Walk | Bicycle | Drive | Bus | Rideshare (e.g. Uber/Lyft) | Rely on others for rides
 | 664 | 624 | 1076 | 533 | 548 | 578
Chart: 
| Work | School | Retail Goods and Services (e.g Shopping, Dining Out) | Medical Appointments | Visiting friends/family
 | 866 | 631 | 965 | 849 | 838
What is your usual destination when using your #1 ranked mode of transportation (Rank from 1-5 with 1 being where you travel most often and 5 being where you travel least often)?
How do you usually travel from place to place? (Rank from 1-6 with 1 being the most frequently used mode of transportation and 6 is the least used)

## Slide 48: Driver Behavior and Needs
Chart: 
| Roadway design | People driving under the influence of alcohol, drugs, medications or other substances | Pedestrians and bicyclists sharing the roadway | People not wearing seatbelts | Aging drivers | Motorcyclists | Commercial vehicles operating on local roads | Speeding and aggressive driving | Teen drivers | People using cell phones or doing other activities while driving | Inadequate roadway lighting or traffic signals | Construction or utility work zones | People who do not know the “rules of the road”
 | 0.17615 | 0.23028 | 0.27248 | 0.011009 | 0.43028 | 0.045872 | 0.14128 | 0.59266 | 0.048624 | 0.64037 | 0.14587 | 0.066055 | 0.40917
Chart: 
| Reducing speeds on major roads through design and traffic signalization strategies | Providing better bicycle facilities including wider bicycle lanes and separated bike paths | Making major roads safer for pedestrians (e.g. improving intersection design, providing marked crosswalks, better lighting | Improving rural roads (e.g. wider shoulders, better signs and pavement markings) | Improving roadway lighting | Increased traffic enforcement
 | 976 | 980 | 982 | 988 | 977 | 1031
Of the items below, which are your top three safety concerns about traveling in Collier County (Choose three)
What is your level of support for the following safety improvements? (Rank each from 1 to 5, with 1 being the most support and 5 being the least support)

## Slide 49: Bicycle/Pedestrian Demand
Chart: 
| Daily | More than 4 times a week | 2-4 times a week | Once a week | Less than once a month
 | 0.17037 | 0.071296 | 0.16759 | 0.12222 | 0.46852
Chart: 
| Daily | More than 4 times a week | 2-4 times a week | Once a week | Less than once a month
 | 0.26131 | 0.087719 | 0.18652 | 0.14866 | 0.31579
How often do you walk and/or ride a bicycle? (choose one)
How often do you walk? (choose one)

## Slide 50: Walking/Biking Comfort Level
Chart: 
| Strongly agree | Somewhat agree | Somewhat disagree | Strongly disagree | No opinion
 | 0.039595 | 0.16575 | 0.1814 | 0.33517 | 0.27808
Chart: 
| Strongly agree | Somewhat agree | Somewhat disagree | Strongly disagree | No opinion
 | 0.14299 | 0.39022 | 0.17712 | 0.1393 | 0.15037
In general, I feel safe and comfortable while riding a bicycle in Collier County. (Choose one)
In general, I feel safe and comfortable while walking in Collier County. (Choose one)

## Slide 51: Walking/Biking Behavior
Chart: 
| Strongly agree | Somewhat agree | Somewhat disagree | Strongly disagree | No opinion
 | 0.094756 | 0.35511 | 0.24011 | 0.24471 | 0.065317
Chart: 
| Strongly Agree | Somewhat Agree | Somewhat Disagree | Strongly Disagree | No Opinion
 | 0.056933 | 0.3214 | 0.30762 | 0.24793 | 0.066116
In general, Collier County pedestrians and bicyclists do a good job following the rules of the road. (Choose one)
In general, Collier County drivers are courteous about sharing the road with pedestrians and bicyclists (Choose one)

## Slide 52: Biking Needs
Chart: 
| More bicycle lanes | More bicycle lanes that are physically separated from vehicle traffic | More multi-use paths | More low-speed neighborhood routes | Make it easier to cross highways and high-speed streets | More convenient and available bicycle parking | Start a bicycle sharing program | More education for motorists and bicyclists about sharing the roadway | Better enforcement of speed limits | Reducing distracted driving
 | 0.20474 | 0.70427 | 0.29668 | 0.11659 | 0.31848 | 0.054028 | 0.042654 | 0.25308 | 0.23791 | 0.45213
What could be done to make bicycling safer in Collier County. (Choose three)